## Slide 1
GridWatch
Power outage prediction & grid equipment failure advisor
U1 / IBM Bobathon 2026
Working local prototype
01
Notes: Based on the supplied U1 problem statement. Team identity is pending.

## Slide 2
The operator decision
Which asset needs attention before the next outage?
Sensor condition and weather inform likelihood.
Customer exposure and critical sites inform priority.
Crew skills and shift capacity constrain the response.
02
Notes: Source: Industry Problem Statements - 2026.pdf, U1. No cost savings are claimed.

## Slide 3
Prediction and planning
Real ETT observations train a 24-hour oil-temperature forecast.
A separate simulator trains the failure classifier.
The advisor combines risk with fictional grid impact.
The planner proposes jobs and crew staging locations.
03
Notes: ETT source: https://github.com/zhouhaoyi/ETDataset. The temperature model is separate from the synthetic outage model.

## Slide 4
Measured holdout results
Real temperature forecast
1.63°C MAE versus 1.71°C persistence baseline
Synthetic failure classifier
0.772 average precision versus 0.512 threshold baseline
Both benchmarks use later-time test periods.
04
Notes: Source: models/metrics.json generated by src/train.py. ETT test n=3446, synthetic test n=2556. Synthetic event prevalence 43.23%. Results do not establish real-world outage accuracy.

## Slide 5
IBM Bob integration
Bob calls the local GridWatch MCP server.
assess_grid_risk returns probabilities, evidence and crew plans.
get_model_evaluation returns the measured benchmarks.
Bob can produce a brief grounded in these tool results.
05
Notes: Official configuration: https://bob.ibm.com/docs/ide/configuration/mcp/mcp-in-bob. Signed-in IBM Bob UI verification is a separate pending step.

## Slide 6
Field validation and impact
The prototype makes priorities and resource gaps inspectable.
Next: obtain timestamped utility failures and archived forecasts.
Validate on later periods and unseen equipment.
Measure false alerts, lead time and recall at a crew budget.
No live dispatch, validated outage accuracy or savings are claimed.
06
Notes: Source: docs/model-card.md. This is a proposed validation plan, not completed field work.